## Slide 1: IMAGE DENOISE
Implementation and analysis of noise reduction algorithms in image processing

## Slide 2: I N T R O D U C T I O N
Images are one of the important part of today’s era of digital world.
Inventions and discoveries of new methodology in the field of computer science has made humans capable of extracting information from any form of data for e.g. text data, image data, video data etc.
Image noise is random variation of brightness or color information in images, and is usually an aspect of electronic noise.
Image noise can result in bad user experience, difficulty in information extraction from image which in turn causes LOSS of information.

## Slide 3: WHAT IS LOSS ?
Mathematically a loss function or cost function maps an event or values of one or more variable into real number intuitively representing some cost associated with the event.
Therefore, the loss is the numerical analysis of amount of noise present in the image with respect to the ideal image.

## Slide 4: CAUSE OF NOISE
Image noise can arise due to many factors. Some of the common cause of image noise are
  Fluctuating voltage levels
  Heat levels
  Sensor Illumination Levels
  High ISO
  Analog-to-digital conversion can generate error in some pixels
  Natural inherent variation in photons striking each pixel at any time
  Sensor readout is sampled or quantized
  Due to natural or man-made signals interferes with the recorded signal
Image noise arises primarily in underexposed footage as pixels have little light fluctuation to report in the intended image but are being over-amplified by boosted ISO values.

## Slide 5: MOTIVATION
Availability of vast ranges of problem statements present in the process of image processing.
Images are very good source of data in medical research and deep learning models and due to noise or pixel errors their efficiency could be decreased.
Therefore we are planning to remove these noise and pixel errors from images to get better accuracy and would try to avoid any problems or harm(in case of medical research output) to anyone.

## Slide 6: TYPES OF NOISE
Gaussian Noise: Gaussian noise caused by natural sources such as thermal vibration of atoms and discrete nature of radiation of warm objects.
Salt and Pepper Noise (Impulsed Valued Noise): This is also called data drop noise because statistically its drop the original data values.
Speckle Noise: This noise is multiplicative noise. Their appearance is seen in coherent imaging system such as laser, radar and acoustics etc..
White Noise: Noise is essentially identified by the noise power. Noise power spectrum is constant in white noise.
Brownian Noise: Colored noise has many names such as Brownian noise or pink noise or flicker noise or 1/f noise.

## Slide 7: Continued….
Periodic Noise: This noise is generated from electronics interferences, especially in power signal during image acquisition.
Quantization Noise: Quantization noise appearance is inherent in amplitude quantization process.
Photon Noise: The appearance of this noise is seen due to the statistical nature of electromagnetic waves such as x-rays, visible lights and gamma rays.
Structured Noise: Structured noise are periodic, stationary or non-stationary and aperiodic in nature.
Gamma Noise: Gamma noise is generally seen in the laser based images. It obeys the Gamma distribution.
Rayleigh Noise: Rayleigh noise presents in radar range images.

## Slide 8: WHY REDUCE THE NOISE
Noise are the unwanted element in the image, the advantages of reducing image noise are
  Less unwanted elements in image
  Better image quality
  Improved data for image processing machine learning or deep learning models

## Slide 9: METHODOLOGY
In first step we would be taking input in “.bmp” format and make array of pixels of noisy image.
Second step we will generate filters like Gaussian filter if needed to apply them on image.
Now we have to apply the image denoising(filtering) algorithm that is basically either convolving a filter or apply some statistical techniques directly on the noisy image array. The result of this is the pixel array with reduced noise.
Now we can save these pixel values and convert it to image for output purpose.

## Slide 10: OBJECTIVE
Gaussian, Salt-Pepper and Speckle Noise are the most common ones. Thus are those we are interested in studying.
Our motive is to implement and apply different filtering algorithms and analyze which algorithm or filtering techniques works better comparative to the others on different noises.
The filters that are under our interest are Gaussian, Median and Weiner filters.

## Slide 11: GAUSSIAN NOISE REMOVAL
The Gaussian Noise removal algorithm works on the particular density formula.
First the Gaussian filter is generated with a given filter size and the standard deviation. The standard deviation defines how strong the filtering effect will be.
After filter generated, the image array is convolved with the filter with a sliding window method.

## Slide 12: Continued….
The algorithm for filter generation is:
gaussianFilterGenerate
set the value of sigma //standard deviation h <- filter height w <- filter width initialize gauss_filter with (h x w) matrix of zeros m = floor(h/2) n = floor(w/2)
for x in -m to m do for y in –n to n: do x1 = 2*pi*(sigma**2) x2 = exp(-(x * x + y * y)/(2*sigma*sigma)) gauss_filter[x + m, y + n] = (1/x1)*x2 return gauss_filter

## Slide 13: Continued….
The algorithm for applying the filter.
applyFilter
imageArray<-image //read image as 3D array
iHeight <- image height
iWidth <- image width
filter<-gauss_filter //generate gauss filter
fHeight <- filter height
fWidth <- filter width
newHeight <- iHeight-fHeight+1
newWidth <- iWidth-fWidth+1

## Slide 14: Continued….
newImage<-imageArray //initialize 3D array of dimensions [newHeight x newWidth x 3] (for RGB)
//applying convolution
for i <- 0 to newHeight
do for j <- 0 to newWidth
do for h <- i to i + fHeight
do for (w <- j to j + fWidth
do newImage[i][j][0] += filter[h-i][w-j]*image[h][w][0]
newImage[i][j][1] += filter[h-i][w-j]*image[h][w][1]
newImage[i][j][2] += filter[h-i][w-j]*image[h][w][2]
return newImage

## Slide 15: FLOWCHART (maybe….)